## Slide 1
VerySimpleCPU
Instruction Set Simulator (ISS)
1/7

## Slide 2
How to run:
  Download everything through the link at: https://www.dropbox.com/sh/df99f5vrt0wahnw/AAAoo9oXUtwCUq0DKeOjQbg0a?dl=0
  Open a cmd window
  Type: VerySimpleCPU programFileName.asm then type r
  You may also type: VerySimpleCPU programFileName.asm > log then type r
VerySimpleCPU.exe is an ISS (i.e., simulation model) written in C.
  Takes a program file, coded in VerySimpleCPU assembly language, as input,
  Reads VerySimpleCPU instructions,
  Executes the instructions, and
  Writes results on to the command window as well as text files.
Provides a debugging environment for VerySimpleCPU programmers.
2/7

## Slide 3
Input File:
  VerySimpleCPU assembly program file
Output Files (in relation to simulation). :
  memin.txt: Contains the memory contents before execution of the program.
  memoutd.txt: After execution of the program, contains the memory contents in decimal.
  memouth.txt: After execution of the program, contains the memory contents in hexadecimal.
In addition, the simulator prints (on the screen) the memory contents before and after execution of each instruction.
3/7

## Slide 4
Example: Summation
A code written in a high-level programming language:
  *103 = *100 + *101 + *102
Can be also written as
  *103 = *100
  *103 = *103 + *101
  *103 = *103 + *102
3
7
4
4/7

## Slide 5
Example: (cont’d)
The program written in VerySimpleCPU assembly language (sample.asm):
  0: CP 103 100
  1: ADD 103 101
  2: ADD 103 102
  3: BZJi 4 0
  4: 3
  100: 3
  101: 7
  102: 4
5/7

## Slide 6
Example: (cont’d)
Running the ISS at command line:
  VerySimpleCPU.exe sample.asm r
Output of the simulator
6/7

## Slide 7
Example: Output Files
7/7